Functional Safety Concept Lane Assistance
Document Version:1.0
Template Version 1.0, Released on 2017-06-21

Document history

Date	Version	Editor	Description
21.08.2017	1.0	Y.Wiyogo	Initial document
23.08.2017	1.1	Y.Wiyogo	Complete the functional safety concept tables
24.08.2017	1.2	Y.Wiyogo	Update paragraph position

Table of Contents

Purpose of the Functional Safety Concept
The purpose of the functional safety concept is to describe the implementation of the independent safety solutions for a defined item.

Inputs to the Functional Safety Concept
Safety goals from the Hazard Analysis and Risk Assessment

ID	Safety Goal
Safety_Goal_01	The oscillating steering torque from the lane departure warning shall be limited
Safety_Goal_02	The lane keeping assistance function shall be time limited and the additional steering torque shall end after a given time interval so that the driver cannot misuse the system for a autonomous driving.
Safety_Goal_03	The lane detection shall not be activated if the detection for a certain environment is not reliable.
Safety_Goal_04	A sudden strong torque shall be avoided.

Preliminary Architecture

Description of architecture elements

Element	Description
Camera Sensor	A sensor for aquiring environment information as image.
Camera Sensor ECU	A processor chip for processing the acquired image data.
Car Display	A display device for visualizing the activation of the function to the driver.
Car Display ECU	A processor chip for processing the data from the camera sensor ECU
Driver Steering Torque Sensor	A sensor that acquires the torque value of the steering wheel
Electronic Power Steering ECU	A processor chip for processing data from camera sensor ECU and torque sensor.
Motor	An electric motor that interpret the EPS ECU data to control the steering wheel

Functional Safety Concept
The functional safety concept consists of:
- Functional safety analysis
- Functional safety requirements
- Functional safety architecture
- Warning and degradation concept
Functional Safety Analysis

Malfunction ID	Main Function of the Item Related to Safety Goal Violations	Guidewords (NO, WRONG, EARLY, LATE, MORE, LESS)	Resulting Malfunction
Malfunction_01	Lane Departure Warning (LDW) function shall apply an oscillating steering torque to provide the driver a haptic feedback	MORE	The lane departure warning function applies an oscillating torque with very high torque amplitude (above limit)
Malfunction_02	Lane Departure Warning (LDW) function shall apply an oscillating steering torque to provide the driver a haptic feedback	MORE	The lane departure warning function applies an oscillating torque with very high torque frequency (above limit)
Malfunction_03	Lane Keeping Assistance (LKA) function shall apply the steering torque when active in order to stay in ego lane	NO	The lane keeping assistance function is not limited in time duration which leads to misuse as an autonomous driving function.

Functional Safety Requirements

Lane Departure Warning (LDW) Requirements:

ID	Functional Safety Requirement	ASIL	Fault Tolerant Time Interval	Safe State
Functional / Safety / Requirement / 01-01	The lane keeping item shall ensure that the lane departure oscillating torque amplidute is below Max_Torque_Amplitude	C	50 ms	Turn off LDW
Functional / Safety / Requirement / 01-02	The lane keeping item shall ensure that the lane departure oscillating torque frequency is below Max_Torque_Frequency	C	50 ms	Turn off LDW

Lane Departure Warning (LDW) Verification and Validation Acceptance Criteria:

ID	Validation Acceptance / Criteria and Method	Verification Acceptance / Criteria and Method
Functional / Safety / Requirement / 01-01	Set oscillating torque amplitude to Max_Torque_Amplitude causes the light warning to be turned on	when the torque amplitude crosses the limit, the lane assistance output is set to zero within the 50 ms fault tolerant time interval
Functional / Safety / Requirement / 01-02	Set oscillating torque frequency to Max_Torque_Frequency causes the warning light to be turned on	when the torque frequency crosses the limit, the lane assistance output is set to zero within the 50 ms fault tolerant time interval

Lane Keeping Assistance (LKA) Requirements:

ID	Functional Safety Requirement	ASIL	Fault Tolerant Time Interval	Safe State
Functional / Safety / Requirement / 02-01	The electronic power steering ECU shall ensure that the lane keeping assistance torque is applied for only Max_Duration.	D	500 ms	Turn off LKA

Lane Keeping Assistance (LKA) Verification and Validation Acceptance Criteria:

ID	Validation Acceptance / Criteria and Method	Verification Acceptance / Criteria and Method
Functional / Safety / Requirement / 02-01	Let the LKA active until the Max_Duration, and the warning light has to be turned on	when the time duration exceeds the limit, the lane assistance output is set to zero within the 500 ms fault tolerant time interval

Refinement of the System Architecture

Allocation of Functional Safety Requirements to Architecture Elements

ID	Functional Safety Requirement	Electronic Power Steering ECU	Camera ECU	Car Display ECU
Functional / Safety / Requirement / 01-01	The lane keeping item shall ensure that the lane departure oscillating torque amplidute is below Max_Torque_Amplitude.	x
Functional / Safety / Requirement / 01-02	The lane keeping item shall ensure that the lane departure oscillating torque frequency is below Max_Torque_Frequency.	x
Functional / Safety / Requirement / 02-01	The electronic power steering ECU shall ensure that the lane keeping assistance torque is applied for only Max_Duration.	x

Warning and Degradation Concept

ID	Degradation Mode	Trigger for Degradation Mode	Safe State invoked?	Driver Warning
WDC-01	turn off the function	Is_Max_Torque_Exceeded	Yes	Turn on warning light on car display
WDC-02	turn off the function	Is_Max_Duration_Exceeded	Yes	Turn on warning light on car display